## Slide 1: Mapping Connectivity Experiences from the use of AGCOM’s Broadband Map
Aldo Milan - AGCOM

## Slide 2: The official database of all Internet access networks available across the national territory
It enables the analysis of broadband infrastructure deployment at address level and supports comparative assessments of technologies and connection speeds. This information can help identify the available Internet infrastructure at any location and assist public authorities in defining policies to bridge the digital divide
Broadband Map

## Slide 3
State of the connectivity
Detect the local availability of telephony and data services and identify the offered speeds for: Copper, Fiber and Wireless Technologies
Produce summary indicators at various territorial levels to identify areas ready for the transition to copper network alternatives
Support the development of regulation and identify potential remedies required to ensure a sustainable copper switch-off

## Slide 4
Reliability – Data must be accurate and trustworthy
Resolution level – Mapping must be detailed and granular
Timely updates – Data should be continuously and regularly updated
Completeness – All network infrastructures must be included
Fexibility – BBmap can’t impose defininitions but it should adapt to local process
Key Requirements

## Slide 5
Metrics and Targets
Coverage is usually analyzed in terms of households covered
Depending on the accounting conventions applied, reported coverage may reach 100% or plateau just above 90%
For example, the European Commission’s Digital Decade targets aim for 100% coverage
However, detailed address-level checks may still reveal unserved households, even in areas classified as served — highlighting the challenge of reaching the last households
Population Dispersion Analysis (Italy)
According to national statistical data, about 93% of the population is concentrated in only 7% of the national territory
Extending wired coverage beyond this threshold is increasingly difficult and economically inefficient

## Slide 6: Focus: BBmap components 1/2
ESRI Enterprise
ESRI AGOL
arcgis.com
ESRI AGOL
arcgis.com
ESRI Enterprise
Atoll Simulatore
ESRI Desktop
Location Tools (Egon)
AWS
SNS Family Transfert Lambda
AWS
Storage Compute Network Security
ESR AOL arcgis.com
Custom BBmap Apps
Open source Desktop
Open Source Postgres Postgis
Freeware Open source GIS Server
Level Platform
Level Infrastructure
Level Application
Google Play
Google
Custom Android App
AWS AI DB
ESRI AGOL
arcgis.com

## Slide 7: Focus: BBmap components 2/2
The system integrates both licensed components and open-source solutions
In recent years, development efforts have increasingly focused on open source, across all layers of the technology stack
The architecture is designed to be modular and adaptable, allowing for low-investment evolutions in response to changing needs
Particular attention is paid to maintenance and upgrade costs: a sophisticated system with high update costs risks becoming unsustainable in the long term

## Slide 8: Focus: managing geo positions 1/2 Key classes and relations
A - Unique Grid-Code
Geo Coordinates
B - Unique Address Code
Textual Description (e.g. a postal address)
entry point
entry point
entry point
entry point
main output
secondary output
functional output
0, 1
n
0,m
1
1
p
spacial based coding
toponymy based coding

## Slide 9: Focus: managing geo positions 2/2 A scalable path: from essential functions to advanced capabilities
Geo Coordinates
Textual Description
Common geocoding process
Geo Coordinates
Textual Description
B - Unique Address Code
toponymy based coding
A - Unique Grid-Code
Geo Coordinates
B - Unique Address Code
Textual Description
topographic based coding
toponymy based coding
Introduced in 2015-2016 to support wholesale regulated market (and reduce disputes)
Adopted with Incumbent’s commitments
Introduced in 2019-2020 to support general mapping (multiple infrastructure) and national vouchers
Math: F(«Textual Description») → R2
Math: P(a,b) – Best matching

## Slide 10: Service vs Infrastructure Mapping
Infrastructure data is sensitive and must be handled with care.
It is essential to distinguish between service availability (what is offered to end users) and the underlying infrastructure (which may include commercially or nationally sensitive elements).
The mapping system must be both flexible and robust, capable of adapting to local requirements and regulatory constraints.
Different levels of data security and access control must be ensured.
Not all geographic databases can or should be exposed on the open web — data exposure must be selective and risk-aware.

## Slide 11: Focus: Estimate the speed – case FTTC

## Slide 12: Focus: estimate the speed – Case FTTH
2.5 Gbit/s shared by 64 users
Maximum load: 2.5/64= 39 Mbit/s (clearly not realistic)
With traffic model we get higher speeds
Chart: Speed model
| 1.7 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 2391.2 | 2372 | 2308 | 2244 | 2180 | 2116 | 2052 | 1988 | 1924 | 1860
Gpon Splitting

## Slide 13: Focus: Estimate the speed – Case 5G
90 Mbps
540 Mbps
Deterministic model
  X, Y, Z always active (full buffer)
  No other traffic
  Instantaneous rates:
X
Y
Z
210 Mbps
Traffic model
  Average Cell Load:
  Peak rates:

## Slide 14
a.milan@agcom.it